Atmega 328: the first 0x200 bytes. These are reserved for user data

Bytes 0-1	First address available for numeric data
Byte 2	Number of bytes used for numeric data
Bytes 3-4	First address reserved for the application
Bytes 5-0x1FF	Available for strings and numeric data

As supplied on the project pcb, bytes 5 to 0x1FB are occupied by strings.
No space is reserved for use by the mini-OS and no numeric data is stored.
Locations 0x01FC, D, E and F are unused.

Atmega 328: The second 200 bytes These are reserved for use by the mini-OS
Bytes 0x200 – 0x3F6 contain a copy of the strings required to use the Atmega 168 as a programmer.
0x3F7 to 0x3FA: These 4 bytes are not used.
0x3FB	controls display intensity
0x3FC	contains 1 for diagnostic mode (user pressed 'x' at the “p/r...” prompt) otherwise contains 0.
0x3FD contains the default value of OSCCAL (supplied by Atmel)
0x3FE and 0x3FF contain the user calibration values of OSCCAL.

Atmega 168 bytes 0-0x1FF

Bytes 0 – 0x1F6 :	These contain strings used when the Atmega 168 is programmed with “1_ATMEGA_Programmer_V2.29A” for updating the mini-OS or programming the Atmega 328 EEPROM.
Note: this space can be overwritten by project SW and the strings restored when needed.

0x1F7 and 0x1F8	User cal byte
0x1F9	Default calibration byte
0x1FA – 0x1FD	4 unused bytes
0x1FE and 0x1FF	Seed for 16 bit PRN generator
Modified as below

0x1FF PRN generator random number HB
0x1FE PRN generator random number LB
0x1FD PRN generator random number HB
0x1FC PRN generator random number LB
0x1FB PRN generator random number HB
0x1FA PRN generator random number LB
0x1F6 PRN EEPROM location offset 0, 1 or 2

Programming the Atmega 168 EEPROM
This is normally done on the programmer pcb using “1_ATMEGA_Programmer_V1.08” running on the Atmega 328.
Echo the “User Prompt” and then press 'P', 'E' and 'W'.
Note:
The Atmega 168 flash should also be programmed with 1_ATMEGA_Programmer_V2.29A.hex”

Programming the Atmega 328 EEPROM
This is normally done on the project PCB using “1_ATMEGA_Programmer_V2.29A.hex” running on the Atmega 168.
When programming the EEPROM press
"E" to program addresses 5 to 0x1FF or
"e" to program addresses 0x200 to 0x3FD or
"D" to delete the entire EEPROM up to 0x3FD (preserves cal bytes)
When verifying the target EEPROM press "r" or "R".

Note: An Atmega 328 programmed with “1_ATMEGA_Programmer_V1.08” can be soldered onto a project pcb if an unprogrammed Atmega 168 has already been soldered in.